## Slide 1
Quantitative Hydrologic Storylines
Project Update Meeting, Reclamation, 17 October 2017
Joe Hamman1, Julie Vano1, Ethan Gutmann1 ,Martyn Clark1,
Jeff Arnold2, Levi Brekke3, Ken Nowak3
NCAR Research Applications Lab
US Army Corps of Engineers Climate Resilience and Preparedness Program
Bureau of Reclamation Research and Development

## Slide 2: Motivation
Slide from Ken Nowak
The challenge is no longer finding information, it is navigating its proper use.

## Slide 3: Motivation
Use whatever runs are available
Select the first run of each global climate model
Rank models using historical performance metrics
Use models that span temperature-precipitation space
Note: global models focus
Past attempts to navigate climate information
Notes: From Rupp et al. Figure 2. Relative error of the ensemble mean of each metric for each CMIP5 GCM. Models are ordered from least (left) to most (right) total relative error, where total relative error is the sum of relative errors from all metrics.

## Slide 4: Navigating climate information

## Slide 5: Navigating climate information
Developing infrastructure, methods, and models to characterize and reduce uncertainty
Developing the bridge for implementation in the water management community

## Slide 6: Outline
Developing infrastructure, methods, and models to characterize and reduce uncertainty
Downscaling
  Existing Methods
  GARD and ICAR Ensemble
  Initial Results
Sampling
  Understanding Ensemble Structure (Clustering)
  Tools for Parametric Ensemble Sampling
Next Steps
  Hydrologic Modeling

## Slide 7: Downscaling
Many existing climate downscaling techniques (e.g. BCSD, LOCA, SDSM, GARD, ICAR, WRF)
Gap in understanding how differences in downscaling techniques translate to differences in hydrologic projections
We’re building a large ensemble of downscaled datasets to test this
  GARDx10+BCSD+LOCA+ICAR=13 DS techniques
  2 RCPs and up to 32 GCMs (all CONUS+)
Downscaling methods
GCMs
Scenario

## Slide 8: Downscaling
Characterizing Uncertainties
  Uncertainty in hydrologic model forcings is the convolution of the downscaling modeling chain
  Important to understand the sources of this uncertainty when choosing methods and developing sampling tools
The current ensemble is allowing us to explore uncertainty in hydrologic forcings

## Slide 9: Downscaling
Spread in Mean Annual Precipitation Change (2080s – 1980s) for the Yakima (WA) and Upper Colorado (CO) basins.
Full Ensemble
GCMs
RCPs
Downscaling
Methods

## Slide 10: Downscaling
Exploring the interactions of GCMs and Downscaling Methods
  Change signals in temperature are consistent between models and downscaling methods
  Precipitation signals are much less consistent, circulation based (methods) GARD tend to show robust drying
  Figure: Heat map comparing change signals (2080s – 1980s) for mean annual temperature and precipitation over the Yakima River Basin.

## Slide 11: Outline
Developing infrastructure, methods, and models to characterize and reduce uncertainty
Downscaling
  Existing Methods
  GARD and ICAR Ensemble
  Initial Results
Sampling
  Understanding Ensemble Structure (Clustering)
  Tools for Parametric Ensemble Sampling
Next Steps
  Hydrologic Modeling

## Slide 12: Ensemble Sampling
Goals:
  Represent uncertainly space
  Avoid analyzing every possible ensemble combination
  Select based on methodological fidelity
Approaches
  Random sample or sample ensemble of convenience
  Regional model performance
  Global model performance

## Slide 13: Ensemble Sampling
http://webext.cgd.ucar.edu/Multi-Case/CVDP_ex/CMIP5-Historical/metrics.html
1
2
3
4
5
Top 5 From Rupp et al.
1
2
3
4
5
Exploring ensemble structure (how do combinations of methods differ?)
Optimal sampling: two examples
  Regional performance
  Global performance
Top 5 From CVDP
Notes: CVDP ranking
CMCC-CMS
HadGEM2-AO
NorESM1-ME
CCSM4
CESM1-BGC
HadGEM2-ES
CanESM2
CMCC-CM
CNRM-CM5
GISS-E2-R-CC
NorESM1-M
BNU-ESM
CESM1-CAM5-1-FV2
CESM1-CAM5
CESM1-FASTCHEM
HadGEM2-CC
IPSL-CM5A-LR
ACCESS1-0
ACCESS1-3
bcc-csm1-1-m
FIO-ESM
GISS-E2-H-CC
GISS-E2-R
IPSL-CM5A-MR
bcc-csm1-1
MRI-ESM1
CESM1-WACCM
FGOALS-g2
GFDL-CM2p1
GFDL-ESM2G
GFDL-ESM2M
IPSL-CM5B-LR
MIROC5
MPI-ESM-LR
GISS-E2-H
MRI-CGCM3
MIROC-ESM
MIROC-ESM-CHEM
CSIRO-Mk3-6-0
inmcm4

## Slide 14: Outline
Developing infrastructure, methods, and models to characterize and reduce uncertainty
Downscaling
  Existing Methods
  GARD and ICAR Ensemble
  Initial Results
Sampling
  Understanding Ensemble Structure (Clustering)
  Tools for Parametric Ensemble Sampling
Next Steps
  Hydrologic Modeling

## Slide 15: Hydrologic Modeling
Hydrologic models
  FUSE, PRMS, and VIC
Status
  VIC/PRMS have been run for BCSD with default and MPR params (VIC only)
  FUSE has been run for BCSD with default parameters
  Preparing inputs for GARD/LOCA/ICAR runs for all models
Figure from Nans Ador’s 2017 EGU poster

## Slide 16: Navigating climate information
Developing infrastructure, methods, and models to characterize and reduce uncertainty
Developing the bridge for implementation in the water management community
Notes: 1. Using engagement with water management community to inform storylines selection
2. Making information about uncertainty more accessible, translatable, and engaging

## Slide 17: Demonstration project
Libby
Dworshak
Engagement to inform storylines
US Army Corps of Engineers Seattle and Walla Walla District Offices
Working with water managers to identify key decisions that climate change information can inform (currently ~10 metrics)
Real world context to explore how location or impact of interest can change model selection

## Slide 18: Accessible information
https://ral.ucar.edu/hap/computational-hydrology

## Slide 19: Dos and Don’ts for using climate change information in water planning and management
Builds on earlier guidance
Modular
Two-way information exchange
Updatable (github)
Version 1.0 in review
Website under construction
Timely, could inform several best practice efforts
Guidelines

## Slide 20: How are people across Reclamation using climate information?
Proposal: Preparing for a Changing Climate: Understanding How Climate Information is Used in Planning and Decision Support across Reclamation (1815)
Project Team: Ian Ferguson, Julie Vano, Martyn Clark, Dan Broman, Subhrendu Gangopadhyay, Marketa McGuire, James Gilbert, Katharine Dahm
Different datasets ???
Different methods ???
Different tools ???
Broad survey across major Reclamation programs, initiatives, and activities, coupled with an in-depth analysis of the Basin Study Program
Figure from Reclamation report on Conveying Climate Change and Vulnerability

## Slide 21: Additional slides…

## Slide 22: Managers provide
Planning horizon
Number of scenarios
Metrics: help select better performing models/techniques
Metrics: some metrics more sensitive to variations in models, parameters
Change thresholds
Ensemble outcomes of interest
Better understanding management decisions can help inform model selection in many ways, including…